## Slide 1: Quantum Computer Emulated on FPGA
Bonga Njamela, University of Cape Town, South Africa
EEE4022S 2024
Supervised by A. Prof. Simon Winberg, Department of Electrical Engineering
30 October 2024

## Slide 2: Introduction
30 October 2024
Quantum Computer Emulated on FPGA
1
Quantum Computing
Quantum computers (QCs) are a recent technology (1982)
QCs the quantum state of particles to represent information
Born's Postulate of Quantum Mechanics
Qubit Representation
Modern quantum computing chips include:
1121 superconducting qubits (2023)
  1225 ytterbium-171 atom qubits (2024)​
  7000 topological qubits (2025)​

## Slide 3: Background
30 October 2024
Quantum Computer Emulated on FPGA
2
For a quantum computer to exist, QCs must have [1]:
  A scalable physical system with well-characterised qubits
  The ability to initialise the state of the qubits to a simple fiducial state
  Long relevant quantum coherence times
  A "universal" set of quantum gates
  A qubit-specific measurement capability
Understanding the Challenges of Fabricating QCs from DiVincenzo's Criteria
Furthermore, quantum communication interfaces must have:
  The ability to interconvert stationary and flying-qubits
  The ability to faithfully transmit flying-qubits between specified locations
[1] DI VINCENZO , D. P. The Physical Implementation of Quantum Computation. Fortschritte der Physik: Progress of Physics 48, 9-11 (2000), 771–783.

## Slide 4: Background
30 October 2024
Quantum Computer Emulated on FPGA
3
Cannot directly model quantum mechanics
Capabilities of FPGAs In Relation to Emulating QCs
Multiple combinational logic blocks offer intrinsic parallelism
Reconfigurable hardware for mapping behaviour of quantum circuits
Multiple resources such as LUTs, DSP, multipliers, adders and registers for performing dense matrix operations associated with quantum gates
FPGA Fabric

## Slide 5: Research Objectives
30 October 2024
Quantum Computer Emulated on FPGA
4
To create an accurate model the initialisation of well-characterised qubits to a fiducial state with sufficiently long decoherence times
The Aims of the Project
To model quantum communication interface for the central QC processing component
To perform key quantum algorithms
QCEm on FPGA

## Slide 6: Methodology
30 October 2024
Quantum Computer Emulated on FPGA
5
Phases in the Research and Design Process

## Slide 7: Methodology
30 October 2024
Quantum Computer Emulated on FPGA
6
System Overview

## Slide 8: Methodology
30 October 2024
Quantum Computer Emulated on FPGA
7
Single-Photon Qubit Initialisation Subsystem
Accurately models qubits in line with DiVincenzo's criteria for QCs

## Slide 9: Methodology
30 October 2024
Quantum Computer Emulated on FPGA
8
Flying-Qubit Detection Subsystem
Models a quantum channel in a QKD network
Uses two transmission modes:
Converts flying-qubits to stationary qubits within a detection window

## Slide 10: Methodology
30 October 2024
Quantum Computer Emulated on FPGA
9
Quantum Algorithm Emulation Subsystem
Defines "universal" set of quantum gates as unitary matrices in MATLAB high-level description
Performs 4 quantum algorithms:
  Quantum Teleportation (QTA)
  3-Qubit Quantum Fourier Transform (QFT)
  5-Qubit Quantum Factoring Algorithm (QFA)
  2-Qubit Quantum Search Algorithm (QSA)

## Slide 11: Methodology
30 October 2024
Quantum Computer Emulated on FPGA
10
Quantum Circuits Describing Algorithms
Quantum Teleportation
3-Qubit Quantum Fourier Transform
Quantum Factoring Algorithm [2]
[2] SKOSANA , U., AND T AME , M. Demonstration of Shor’s Factoring Algorithm for N = 21 on IBM Quantum Processors. Scientific reports 11, 1 (2021), 16599.
Quantum Search Algorithm

## Slide 12: Methodology
30 October 2024
Quantum Computer Emulated on FPGA
11
QAES FPGA Design Flow
[2] SKOSANA , U., AND T AME , M. Demonstration of Shor’s Factoring Algorithm for N = 21 on IBM Quantum Processors. Scientific reports 11, 1 (2021), 16599.

## Slide 13: Methodology
30 October 2024
Quantum Computer Emulated on FPGA
12
User Interface Subsystem
The main function is to allow users to select which quantum experiment they wish to perform
Nexys-A7 Switches
UCT Dev Board

## Slide 14: Results
30 October 2024
Quantum Computer Emulated on FPGA
13
High-Level Description in MATLAB
The unitary matrix operations associated with qubit registers and quantum gates were described using MATLAB
Nexys-A7 Switches

## Slide 15: Results
30 October 2024
Quantum Computer Emulated on FPGA
14
Conversion to SystemVerilog Using HDL Coder
A sfix14_En13 fixed-point conversion was successfully implemented using HDL Coder

## Slide 16: Results
30 October 2024
Quantum Computer Emulated on FPGA
15
RTL Verification
Behavioural and timing verification was performed using waveforms, Simulink models and .dat file outputs

## Slide 17: Results
30 October 2024
Quantum Computer Emulated on FPGA
16
Synthesis in AMD Vivado
Quantum algorithms were successfully synthesised in AMD Vivado and MATLAB to show resource usage

## Slide 18: Results
30 October 2024
Quantum Computer Emulated on FPGA
17
Implementation
Some algorithms were not successfully implemented due to requirement for more IO pins than the available 210 on the board
Quantum gates were successfully implemented

## Slide 19: Results
30 October 2024
Quantum Computer Emulated on FPGA
18
Hardware Design
The full quantum information system is shown below

## Slide 20: Results
30 October 2024
Quantum Computer Emulated on FPGA
19
Summary of Resource Usage

## Slide 21: Conclusion
30 October 2024
Quantum Computer Emulated on FPGA
20
Conclusion and Future Recommendations
Overall, core quantum circuit were successfully performed by the QCEm On FPGA system with minimal resource usage.
The quantum factoring algorithm was not implemented on the hardware but showed the highest resource usage due to large number of quantum gates.
Recommended integration of quantum error correction techniques such as code repetition to carry fixed-point error through the system

## Slide 22: Thank You!
30 October 2024
21
Quantum Computer Emulated on FPGA